## Slide 1: National Weather Service Media Seminar February 2007
The EF Tornado Rating Scale
Jim Kramper
Warning Coordination Meteorologist
National Weather Service, St. Louis, MO
NOAA’s National Weather Service
Notes: Self introduction and introduction of topic.

## Slide 2: Fujita (F) Scale
Dr. Tetsuya Theodore Fujita - 1971
Estimate tornado wind speeds based on damage left behind
F0 - F5 (F6 - F12)

## Slide 3: Fujita (F) Scale Limitations
Lack of damage indicators
Limited account for construction quality and variability
F3 | 158-206 mph | Roofs and walls torn off well-constructed houses
F4 | 207 - 260 mph | Well-constructed housed leveled

## Slide 4: Fujita (F) Scale Problems
Tornadoes were rated in an inconsistent manner
No definitive correlation between damage and wind speed
Overestimate of tornado wind speeds

## Slide 5: Enhanced F (EF) Scale
Texas Tech University Wind Science and Engineering Research Center
Steering Committee
Fujita Scale Forum
  Identify additional damage indicators
  Correlate appearance of damage and wind speed
  Preserve the historical database
  Seek input from users

## Slide 6: EF Scale
28 Damage Indicators (DI)
  Typical Construction
A series of Degrees of Damage (DOD)
  Expected wind speed
  Lower bound wind speed
  Upper bound wind speed

## Slide 7: EF Scale
F scale fastest ¼ mile speed
  3 - Second Gust
Median F speeds were compared to Expected wind speeds: regression analysis
  y = 0.6246x + 36.393 (y = EF, x =F)

## Slide 8: EF Scale
F Scale | 3 sec gust | EF Scale | 3 sec gust
F0 | 45-78 | EF0 | 65-85
F1 | 79-117 | EF1 | 86-109
F2 | 118-161 | EF2 | 110-137
F3 | 162-209 | EF3 | 138-167
F4 | 210-261 | EF4 | 168-199
F5 | 262-217 | EF5 | 200-234

## Slide 9: EF Scale
Recommended EF Scale | 
EF Class | 3 - Second gust speed (mph)
EF0 | 65-85
EF1 | 86-110
EF2 | 111-135
EF3 | 136-165
EF4 | 166-200
EF5 | > 200

## Slide 10: Example Rating
Expected Wind = 97 mph

## Slide 11: EF Scale
Recommended EF Scale | 
EF Class | 3 - Second gust speed (mph)
EF0 | 65-85
EF1 | 86-110
EF2 | 111-135
EF3 | 136-165
EF4 | 166-200
EF5 | > 200